Subject Matter Specification Table

For the contract named:

"Energy saving measures in the company BUILDING SHUTTER SYSTEMS s.r.o. "

The Client specifies special technical conditions for the subject of the contract, which are defined in the document "Subject Matter Specification Table" (separately for each individual part of the contract). The Client defines the characteristics of the requested subject-matter of delivery which the Contractors' offered subject-matter of delivery must meet. The Contractor shall indicate in the technical specifications whether the delivery offered by it meets the requirements set out in the columns by selecting the appropriate option in the 'Meets' column, 'Yes' if the delivery offered meets this requirement and 'No' if the delivery offered does not meet this requirement. In case the Contractor indicates "No" at least once in the technical specifications, they will be excluded for non-compliance. If the Contractor indicates 'Yes' and the evaluation of bids reveals that the goods offered do not meet this requirement, the Contractor may be excluded for non-compliance and breach of the tender conditions. If the Contractor does not fill in either the 'Yes' or the 'No' option, they may be excluded for non-compliance with the terms of reference. The Contractor shall then indicate in the column 'Contractor is offering' the specific value of the parameter (in the same units as the requirement) or a more detailed specification of the delivery offered in relation to the requirement. If the Contractor does not fill in the column 'Contractor offers' and ticks the option 'Yes' in the column 'Meets', it shall be deemed that the delivery offered by the Contractor corresponds exactly to the requirement of the Client, as set out in the columns 'Required parameter' or 'Required value'.

The Contractor will supply 1 piece of new and unused vertical painting line, as specified below.

| Production marking of the subject matter offered by the Contractor: | (bidder to enter the production marking of the machine here) |
| --- | --- |
| Required parameter | Required value | Meets | Contractor is offering |
| Surface finish line specifications |
| Type of line | continous | YES / NO |  |
| Maximum building dimensions of the painting line | 29.750x28.150x10.000 mm | YES / NO |  |
| Maximum building dimensions of the neutralization station | 12.460x6.930x10.000 mm | YES / NO |  |
| Passage profile - product width | min. 300 mm | YES / NO |  |
| Passing profile - product height | min. 7000 mm | YES / NO |  |
| Passage profile - product length | min. 300 mm | YES / NO |  |
| Conveyor speed | min. 1,2 m/min | YES / NO |  |
| Minimum product length | max. 2500 mm | YES / NO |  |
| Number of painted profiles | min. 540 pcs/hour | YES / NO |  |
| Hanger distance | 133 mm | YES / NO |  |
| All documentation for the equipment according to the current legislation in CZ language | yes | YES / NO |  |
| Legislative authorization of the source according to Act 201/2012 Coll. | yes | YES / NO |  |
| Guarantee of varnishing of standard products according to Annex 4 | yes | YES / NO |  |
| Media distribution to the connection points of the technology from the defined connection points | yes | YES / NO |  |
| Chemical pretreatment tunnel parameters |
| Number of chemical pretreatment stages | min. 9 | YES / NO |  |
| Rinsing of parts by cascade system | yes | YES / NO |  |
| Minimum number of cascades for degreasing and deoxidation stages | min. 3 pcs | YES / NO |  |
| Rinsing of parts up to a length of 2.5 by ramps with nozzles | yes | YES / NO |  |
| Control of chemical pretreatment by central control system | yes | YES / NO |  |
| Temperature and pressure measurement in all stages | yes | YES / NO |  |
| Conductivity and pH measurements in the chemical preparation stages | yes | YES / NO |  |
| Conductivity measurements in rinse water tubs | yes | YES / NO |  |
| Heat source for heated tubs | Tube heat exchanger | YES / NO |  |
| Gas-fired boiler for hot water production min. 500 kW including flue | yes | YES / NO |  |
| System for easy cleaning of the heat exchanger | yes | YES / NO |  |
| Insulation of heated pre-treatment stages | yes | YES / NO |  |
| Automatic level control | yes | YES / NO |  |
| Automatic water refilling via cascade | yes | YES / NO |  |
| Minimum length of prechambers of each stage | min. 0,4 m | YES / NO |  |
| Min. length of active zone for deoxidation and degreasing tubs | min. 2,7 m | YES / NO |  |
| Location of pumps | Outside the tubs | YES / NO |  |
| Material of tubs, tunnels and spray wreaths for chemical solution stages | AISI 316 stainless steel | YES / NO |  |
| Guaranteed pre-treatment lifetime min. 5 years | yes | YES / NO |  |
| Material of the active part of the pumps | AISI 316L | YES / NO |  |
| Discharge height of pumps | min. 18 m | YES / NO |  |
| Number of inspection doors | min. 1 pcs | YES / NO |  |
| Insulation thickness of heated tubs | min. 50 mm | YES / NO |  |
| Air extraction outside the production area | yes | YES / NO |  |
| Inspection lighting technology | LED | YES / NO |  |
| Emergency sump integrated in the floor | yes | YES / NO |  |
| Demi-station with a flow rate of min. 12,000 l/h | yes | YES / NO |  |
| Duplex for possible continuous operation without interruption for regeneration | yes | YES / NO |  |
| Automatically controlled regeneration process | yes | YES / NO |  |
| PLC control of the demi-station with output to the master system | yes | YES / NO |  |
| Drying oven parameters |
| Maximum achievable temperature | min. 120°C | YES / NO |  |
| Internal conveyor path in the oven | min. 19 000 mm | YES / NO |  |
| Heat recovery through cooling of products from the curing oven | yes | YES / NO |  |
| Insulation thickness of cladding | min. 200 mm | YES / NO |  |
| Heat exchanger in common with the curing oven | yes | YES / NO |  |
| Control of the curing oven from a central control panel | yes | YES / NO |  |
| Air exhausts included | yes | YES / NO |  |
| Included flue gas path including inspection | yes | YES / NO |  |
| Fume hood at oven inlet | yes | YES / NO |  |
| Air curtains at inlet and outlet | yes | YES / NO |  |
| Conveyor inside the oven in the plane | yes | YES / NO |  |
| Control of the drying oven by a central control system | yes | YES / NO |  |
| Temperature measurement in the kiln at 2 points | yes | YES / NO |  |
| Heating medium | natural gas | YES / NO |  |
| Vypalovací pec |
| Maximum achievable temperature | min. 200°C | YES / NO |  |
| Inner conveyor path in the oven | min. 30 000 mm | YES / NO |  |
| Gas heating capacity | min. 600 kW | YES / NO |  |
| Insulation thickness of cladding | min. 200 mm | YES / NO |  |
| Indirect heating of the curing oven | yes | YES / NO |  |
| Control of the firing oven from the central control panel | yes | YES / NO |  |
| Air exhausts included | yes | YES / NO |  |
| Includes flue gas path including inspection | yes | YES / NO |  |
| Fume hood at oven inlet | yes | YES / NO |  |
| Air curtains at inlet and outlet | yes | YES / NO |  |
| Oven in conveyor plane | yes | YES / NO |  |
| Oven temperature measurement at 2 points | yes | YES / NO |  |
| Heating medium | natural gas | YES / NO |  |
| Cooling of products first in the drying oven and then on the conveyor | yes | YES / NO |  |
| Powder application booth |
| Powder paint recovery using cyclone | yes | YES / NO |  |
| Extraction air volume | min. 34 000 m3/hour | YES / NO |  |
| Filter with automatic dedusting and secondary filter with residual dust limit up to 5 mg/m3 | yes | YES / NO |  |
| Automatic discharge of waste from the filter into the big-bag | yes | YES / NO |  |
| Number of cyclone separators | 2 pcs | YES / NO |  |
| Cabin type | Plastic booth with rotation walls | YES / NO |  |
| Clean room to prevent external influences during painting | yes | YES / NO |  |
| Automatic wall rotation control from PLC | yes | YES / NO |  |
| Number of manipulators | min. 2 pcs | YES / NO |  |
| Min. manipulator speed | 75 m/min. | YES / NO |  |
| Infinitely adjustable manipulator stroke | yes | YES / NO |  |
| Minimum manipulator load capacity 30 kg | yes | YES / NO |  |
| Number of automatic spray guns | min. 18 pcs | YES / NO |  |
| Number of angle heads of automatic spray guns | min. 18 pcs | YES / NO |  |
| Ultrasonic sieve of the feeding centre | yes | YES / NO |  |
| Automatic recuperation/fresh powder switching | yes | YES / NO |  |
| Control of recuperated/fresh powder ratio | yes | YES / NO |  |
| Cabin lighting type | LED | YES / NO |  |
| Minimum intensity of lighting in the cabin | min. 600 lx | YES / NO |  |
| Automatic fire extinguishing system with CO2, including revision | yes | YES / NO |  |
| Ensuring a professional opinion on safety compliance of reserved technical equipment from the Technical Inspectorate of the Czech Republic | yes | YES / NO |  |
| Overhead conveyor |
| Conveyor load capacity | min. 150 kg/m | YES / NO |  |
| Downward orientation of the groove | yes | YES / NO |  |
| Stacking spacing | 133 mm | YES / NO |  |
| Nominal conveyor speed | min. 1,2 m/min | YES / NO |  |
| Continuous conveyor speed control in the range of 0.5 - 3 m/min. | yes | YES / NO |  |
| Automatic conveyor lubrication | yes | YES / NO |  |
| Complete self-supporting structure | yes | YES / NO |  |
| Conveyor control must be via a central control system | yes | YES / NO |  |
| Conveyor ascent/descent | max 30° | YES / NO |  |
| Temperature resistance | min. 220°C | YES / NO |  |
| Inspection piece | yes | YES / NO |  |
| Synchronised platforms for loading and unloading of 2.5 to 7 m large profiles | yes | YES / NO |  |
| Hydraulic sliding of the unloading platform | yes | YES / NO |  |
| Control system |
| Start-up function of all components from a central location | yes | YES / NO |  |
| Option to automatically start the whole unit with a timer | yes | YES / NO |  |
| Minimum touch screen size 15'' | yes | YES / NO |  |
| Possibility to control technological parameters via remote management | yes | YES / NO |  |
| Setting of required parameters (temperature, cleaning cycles) from a central location | yes | YES / NO |  |
| Storage of settings in programs for later use | yes | YES / NO |  |
| On-line access: remote access for the service department, possibility to remotely change the technological parameters of the line or to control technological data | yes | YES / NO |  |
| Data archiving, data can be stored on an external USB flash drive | yes | YES / NO |  |
| Storage of measured data on FTP server | yes | YES / NO |  |
| Complete data storage in XLS (Excel) format | yes | YES / NO |  |
| Language selection on the control panel min. CZ/EN | yes | YES / NO |  |
| Neutralization station |
| Concentrate holding tank with a volume of at least 10 m3 | yes | YES / NO |  |
| Holding tank for rinse water with a minimum volume of 10 m3 | yes | YES / NO |  |
| Automatic NS operation | yes | YES / NO |  |
| Sludge press with 30 plates and plate size min. 470x470 mm | yes | YES / NO |  |
| Quality of the discharged water according to NV No. 401/2015 Coll. | yes | YES / NO |  |
| Equipment for automatic paint removal from hooks |
| Equipment for automatic paint removal from hooks without need to dismount them | yes | YES / NO |  |

I (we), the undersigned     , honestly declare that the above information is true and that the Contractor     , if selected by the Client in the tender, will deliver the goods exactly in accordance with the technical and commercial terms and conditions specified in its bid.

In     on

…………..………………………….

(Name, surname, signature and position of the person authorized  to act on behalf of the Contractor)